## Slide 1: Complements of numbers

## Slide 2: Subtraction using addition
▶ Conventional addition (using carry) is easily implemented in digital computers.
▶ Subtraction by borrowing is difficult and inefficient for digital computers.
▶ It is much more efficient to implement subtraction using ADDITION OF the COMPLEMENTS of numbers.

## Slide 3: r’s Complement
Given a number N in base r having n digits,
The r’s complement of N is defined as
rn
- N.
For decimal numbers the base or r = 10, so the 10’s complement of N is 10n-N.

## Slide 4: 10’s complement
For numbers with base or r=10,
r’s complement is 10’s complement.
The 10’s complement is given by 10n –N
Example:
The 10’s complement of 546700 is 1000000-546700= 453300

## Slide 5: 2’s complement
For binary numbers, r = 2,
r’s complement is the 2’s complement. The 2’s complement of N is 2n - N.

## Slide 6: 2’s complement Example
The 2’s complement of 1011001 is 0100111
The 2’s complement of 0001111 is 1110001
-
-
1 | 0 | 1 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 7: Fast Methods for 2’s Complement
Method 1:
The 2’s complement of binary number is obtained by adding 1 to the l’s complement value.
Example:
1’s complement of 101100 is 010011 (invert the 0’s and 1’s) 2’s complement of 101100 is 010011 + 1 = 010100

## Slide 8: Fast Methods for 2’s Complement
Method 2:
The 2’s complement can be formed by leaving all least significant 0’s and the first 1 unchanged, and then replacing l’s by 0’s and 0’s by l’s in all other higher significant bits.
Example:
The 2’s complement of 1101100 is
0010100
Leave the two low-order 0’s and the first 1 unchanged, and then replace 1’s by 0’s and 0’s by 1’s in the four most significant bits.

## Slide 9: Examples
▶ Finding the 2’s complement of (01100101)2
▶ Method 1 – Simply complement each bit and then add 1 to the result.
(01100101)2
[N] = 2’s complement = 1’s complement (10011010)2 +1
=(10011011)2
▶ Method 2 – Starting with the least significant bit, copy all the bits up to and including the first 1 bit and then complement the remaining bits.
N = 0 1 1 0 0 1 0 1
[N] = 1 0 0 1 1 0 1 1

## Slide 10: (r-1)’s Complement
Given a number N in base r having n digits.
The (r- 1)’s complement of N is defined as (rn - 1) - N .
For decimal numbers the base or r = 10 and r- 1= 9, so the 9’s complement of N is (10n-1)-N

## Slide 11: 9’s complement
For numbers with base or r=10
the (r-1)’s complement is 9’s complement.
9’s complement is given by (10n-1)-N.
Example:
The 9’s complement of 546700 is 999999 - 546700=
453299

## Slide 12: 1’s complement
▶ For binary numbers, r = 2 and (r — 1) = 1, r-1’s complement is the 1’s complement.
▶ The 1’s complement of N is (2n - 1) - N.

## Slide 13: 1’s complement
The complement 1’s of 1011001 is 0100110
-
-
1 | 0 | 1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1 | 1 | 0
The 1’s complement of 0001111 is 1110000
0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0 | 0

## Slide 14: Subtraction using Complements
S